# Lista de sensores
- CATSENSORS - Sensor DL-PR36 IoT LoRaWAN: Medición de alta precisión de Presión, Nivel y Temperatura en Fluidos (0 to 1 bar (relative)) (1570€)
- CATSENSORS - Sensor DL-PR21 LoRaWAN: Nivel, Temperatura y Presión (sonda digital I2C)(-1 to 10 bar) (770€)
- CATSENSORS - Sensor DL-PR26 LoRaWAN: Nivel y Temperatura (sonda digital I2C)(0 to 1 bar) (830€)

- DRAGINO - LSN50v2-D20 -- LoRaWAN Waterproof /Outdoor Temperature (50€)
  - LoRaWAN v1.0.3 Class A
  - Ultra low power consumption
  - Accuracy ±0.5°C (max ±2.0 °C)
  - External DS18B20 Probe (default 2meters)
  - Measure range -55°C ~ 125°C
  - 8500mAh Li-SOCI2 battery
  - Temperature alarm
  - Bands: CN470/EU433/KR920/US915
  - EU868/AS923/AU915/IN865
  - AT Commands to change parameters
  - Uplink on periodically or Interrupt
  - Downlink to change configure

- DRAGINO - LDDS20 LoRaWAN Liquid Level Sensor (63€)
  - LoRaWAN 1.0.3 Class A
  - Ultra low power consumption
  - Liquid Level Measurement by Ultrasonic technology
  - Measure through container, No need to contact Liquid.
  - Valid level range 20mm - 2000mm
  - Accuracy: ±(5mm+S*0.5%) (S: Measure Value)
  - Cable Length : 25cm
  - Bands: CN470/EU433/KR920/US915/EU868/AS923/AU915/IN865
  - AT Commands to change parameters
  - Uplink on periodically
  - Downlink to change configure
  - IP66 Waterproof Enclosure
  - 8500mAh Battery for long term use

- DRAGINO - LDDS75 LoRaWAN Distance Detection Sensor (67€)
  - LoRaWAN 1.0.3 Class A
  - Ultro low power consumption
  - Distance Detection by Ultrasonic technology
  - Flat object range 280mm - 7500mm
  - Cable Length : 25cm
  - Temperature Compensation
  - Bands: CN470/EU433/KR920/US915/EU868/AS923/AU915/IN865
  - AT Commands to change parameters
  - Uplink on periodically
  - Downlink to change configure
  - IP66 Waterproof Enclosure
  - 4000mAh or 8500mAh Battery for long term use

- DINGTEK - LoRaWAN DF550 Top installation Ultrasonic Liquid Level Sensor (+3 años bateria IP66) (72€) (ENLACE)
  - Ultrasonic Technology
  - Detection Range: 200cm/500cm/800cm
  - Blind Area: <20cm
  - Height Error: 3mm
  - LoRaWAN EU868Mhz
  - No rechargeable Battery ER26500 8000mAh @3.6V
  - Battery life: +3 years
  - Operation Temp: -20ª to +70ºC
  - Storage Temperature: -40ºC to +70ºC
  - Waterproof Level: IP66
  - Level Alarm
  - Map Display

- DINGTEK - LoRaWAN DF520 Bottom installation Ultrasonic Liquid Level Sensor (+3 años bateria IP66) (110€) (ENLACE)
  - Ultrasonic Technology
  - Detection Range: 30 mm- 10000mm
  - Blind Area: 30cm
  - Height Error: 3mm
  - Controller MCU: STM32, 32bit ARM core controller
  - LoRaWAN EU868Mhz
  - No rechargeable Battery ER26500 8000mAh @3.6V
  - Battery life: +3 years
  - Operation Temp: -20ª to +70ºC
  - Storage Temperature: -40ºC to +85ºC
  - Waterproof Level: IP66
  - Level Alarm
  - Map Display

- DECENTLAB – DL-PR21-001 Pressure / Liquid Level and Temperature Sensor (566€)
  - Pressure: -1 ... 10 bar, relative
  - Temperature: -40 ... +125 °C
  - Pipe thread: G1/4'', others on request
- DECENTLAB – DL-PR26-001 Pressure / Liquid Level and Temperature Sensor (617€)
  - Pressure: 0 ... 1 bar, relative
  - Temperature: -40 ... +125 °C
- TEKELEK - TEK Aqua LoRa Ultrasonic
- PROESYS - LoRaWAN™ Industrial Pressure Sensor IPS-1
- ELLENEX – RS1-L Sensor de presion (525€)
  - Output 4-20mA/0-5V/0-10V
  - Operating temperature range -10ºC to 70ºC
  - Battery lifetime +10 years
  - Protection rate IP65 /IP67, UV Protected

- LEEFO - T3000-sensor de presión de agua (ENLACE) (55€)
  - Output: 4~20mA, 0~10VDC 0~5V
  - Working temperatures: -40℃~100℃
  - Fuente de alimentación 12-36VDC
  - Precisión 0.25% F.S/0.5% F.S
- HONDETEC – RD-TS-O-01 Turbidimetro Industrial óptico (ENLACE) (356€)
  - Optical principle
  - Tipo de salida: RS485 /0-5V/0-10V/4-20mA output
  - LORA/LORAWAN(EU868MHZ,915MHZ), GPRS, NB-IOT
  - 0-2V/0-5V/0-10V output
  - Tensión de alimentación: 5-24VDC
  - Temperatura de funcionamiento: 0 a 60ºC
  - Rango de 0,1 ~ 1000,0 NTU
  - Garantia de 1 año

- UTMOST – JPG7 Sensor de presión de agua de 0-10V de salida analógica (ENLACE)(54€-71€)
  - Output: 4~20mA, 0~10VD 0~5V
  - Working temperatures: -40℃~100
  - Precisión 0.5% F.S
  - Fuente de alimentación 10 ~ 30V o 5V DC
  - ISO9001/CE/ROHS

HOLYKELL – HPT604 Sensor de presión de nivel de agua (ENLACE) (69€-129€)

salida 0.10 voltios